## Slide 1
Basic switching concepts circuit switching message switching packet switching

## Slide 2: Switching
Circuit Switching
  Fixed and mobile telephone network
    Frequency Division Multiplexing (FDM)
    Time Division Multiplexing (TDM)
  Optical rings (SDH)
Message Switching
  Not in core technology
  Some application (e.g. SMTP)
Packet Switching
  Internet
  Some core networking technologies (e.g. ATM)

## Slide 3: Time Division Multiplexing
time
8 bits
Link: 64 kbps
Source rate: 64 kbps
125 s
time
Link: 256 kbps
time
Link: 256 kbps
Control information inserted for framing – result: 4x64 > 256!

## Slide 4: Circuit Switching (i)
switch
switch
time
#1
#2
…
#8
#1
#2
…
#8
frame
TDM slot
ctrl
…
TDM link
Time Division Multiplexing

## Slide 5: Circuit Switching (ii)
switch
switch
#1
#2
…
#8
IN_A
OUT_A
OUT_B
IN_B
#1
#2
…
#8
IN_A
IN_B
#1
#2
…
#8
#1
#2
…
#8
OUT_A
OUT_B
SWITCHING
TABLE
A,1
B,2
A,3
B,4
A,4
A,2
B,1
B,1
B,4
B,3
B,6
A,1
B,7
B,5
IN
OUT
Table setup: upon signalling

## Slide 6: Circuit Switching Pros & Cons
Advantages
  Limited overhead
  Very efficient switching fabrics
    Highly parallelized
Disadvantages
  Requires signalling for switching tables set-up
  Underutilization of resources in the presence of bursty traffic and variable rate traffic
Bandwidth waste

## Slide 7: Example of bursty traffic (ON/OFF voice flows)
On (activity) period
OFF period
VOICE SOURCE MODEL for conversation (Brady):
average ON duration (talkspurt): 1 second
average OFF duration (silence): 1,35 seconds
Efficiency = utilization % = source activity

## Slide 8: Message vs Packet Switching
Message Switching
  One single datagram
message
header
header
packet
packet
packet
p
header
header
header
Packet Switching
  Message chopped in small packets
  Each packet includes header
    like postal letters! Each must have a specified destination data
Message switching overhead lower than packet switching

## Slide 9: Message vs Packet Switching
Message Switching
  One single datagram
    either received or lost
    One single network path
message
header
header
packet
packet
packet
p
header
header
header
Packet Switching
  Many packets generated by a same node and belonging to a same destination
    may take different paths (and packets received out of order – need sequence)
    May lose/corrupt a subset (what happens on the message consistency?)
Message switching: higher reliability, lower complexity
But sometimes message switching not possible
(e.g. for real time sources such as voice)

## Slide 10: Message/packet Switching vs circuit switching
router
router
mesg/pack
header
Router:
- reads header (destination address)
- selects output path
Advantages
  Transmission resources used only when needed (data available)
  No signalling needed
Disadvantages
  Overhead
  Inefficient routing fabrics (needs to select output per each packet)
  Processing time at routers (routing table lookup)
  Queueing at routers

## Slide 11: Link delay computation
Tx delay
B/C
Router
Transmission delay:
  C [bit/s] = link rate
  B [bit] = packet size
  transmission delay = B/C [sec]
Example:
  512 bytes packet
  64 kbps link
  transmission delay = 512*8/64000 = 64ms
Propagation delay – constant depending on
  Link length
  Electromagnetig waves propagation speed in considered media
    200 km/s for copper links
    300 km/s in air
other delays neglected
  Queueing delay
  Processing delay
time
sender
time
receiver
Tx delay
B/C
Prop
delay
Delay components:
    Processing delay
    Transmission delay
    Queueing delay
    Propagation delay

## Slide 12: Message Switching – delay analysis
Router 1
320 Kbps
320 Kbps
320 Kbps
Router 2
Tx delay
M/C
time
time
Tx delay
M/C
Prop
delay
Tx delay
M/C
Prop
delay
Tx delay
B/C
Prop
delay
Example: M=400.000 bytes
Header=40 bytes
Propagation Tp = 0.050 s
Del = 3M/C + 3Tp = 30,153 s

## Slide 13: Packet Switching – delay analysis
Router 1
320 Kbps
320 Kbps
320 Kbps
Router 2
Tx delay
Mh/C
time
time
Prop
delay
Tx delay
Ph/C
Tx delay
Mh/C
Packet P = 80000 bytes
H = 40 bytes header  Ph = 80040
Message: M=400.000 bytes  Mh=M+M/P*H=40200 bytes
Propagation Tp = 0.050 s
Del = Mh/C + 3P + 2Ph/C = 14,157 s
Prop delay
Tx delay
Ph/C
Prop delay
But if packet size = 40 bytes, Del = 20,154s!

## Slide 14: Other example (different link speed)
Time to transmit 1 MB file
Message switching (assume 40 bytes header)
  1MB = 1024*1024 bytes = 1.048.576 bytes = 8.388.608 bits
  Including 40 bytes (320 bits) header: 8.388.928
  Neglecting processing, propagation & queueing delays:
    D = 32.76 + 8.19 + 4.10 + 32.77 = 77.83s
Packet switching (40 bytes header, 1460 bytes packet)
  718,2  719 packets
  total message size including overhead = 8.618.688
  Just considering transmission delays (slowest link = last – try with intermediate, too)
    D = 0.07 + 33.67 =33.74s
Key advantage: pipelining reduces end to end delay versus message switching!
Router 1
Router 3
256 Kbps
1024 Kbps
2048 Kbps
256 Kbps

## Slide 15: Statistical Multiplexing the advantage of packet switching
#1
#2
Circuit switching:
Each slot uniquely
Assigned to a flow
#3
#4
#1
#2
#3
#4
Full capacity does not imply full utilization!!
idle
idle
idle
idle
Packet switching:
Each packet grabs
The first slot available
More flows than nominal capacity may be admitted!!

## Slide 16: Packet Switching overhead vs burstiness
Overhead for voice sources at 64 Kbps
Source rate: 64 kbps
16 ms voice samples = 62,5 samples per sec, each sample = 1024 bit
Assumption: 40 bytes header
PACKETIZATION for voice sources (Brady model, activity=42.55%):
Assumptions: neglect last packet effect
On (activity) period
OFF period

## Slide 17: Packet switching overhead
Header: contains lots of information
  Routing, protocol-specific info, etc
  Minimum: 28 bytes; in practice much more than 40 bytes
    Overhead for every considered protocol: (for voice: 20 bytes IP, 8 bytes UDP, 12 bytes RTP)
Question: how to minimize header while maintaining packet switching?
Solution: label switching (virtual circuit)
  ATM
  MPLS
packet
header

## Slide 18
Circuit Switching (again)
switch
switch
#1
#2
…
#8
IN_A
OUT_A
OUT_B
IN_B
#1
#2
…
#8
IN_A
IN_B
#1
#2
…
#8
#1
#2
…
#8
OUT_A
OUT_B
SWITCHING
TABLE
A,1
B,2
A,3
B,4
A,4
A,2
B,1
B,1
B,4
B,3
B,6
A,1
B,7
B,5
IN
OUT
Switching table: route packet coming from
Input A, position 1 to output B position 2
A1, B2 = physical slots, can be used only by THAT source.
Let them be “virtual” (labels on packet!)

## Slide 19
Label Switching (virtual circuit)
switch
switch
IN_A
OUT_A
OUT_B
IN_B
IN_A
IN_B
OUT_A
OUT_B
21
22
10
14
16
19
33
LABEL
SWITCHING
TABLE
10
A
14
B
16
B
19
B
21
B
22
B
33
A
Label-IN
OUT
61
61
12
87
10
32
13
Label-OUT
61
13
61
12
10
32
87
Condition: labels unique @ input
Advantage: labels very small!!
(ATM technology overhead: only 5 bytes for all info!)
KEY advantage: no reserved phy slots!
(asynchronous transfer mode vs synchronous)

## Slide 20: Statistical mux efficiency (for simplicity, fixed-size packets)
queueuing
3 flows
2 circuits
Queueuing build-up

## Slide 21: Statistical mux analysis
Very complex, when queueing considered
  Involves queueing theory
  Involves traffic time correlation statistics
Very easy, in the (worst case = conservative) assumption of unbuffered system
  In practice, burst size long with respect to buffer size
Depends only on activity factor 
High corr
Low corr

## Slide 22: Statistical mux analysis (i) unbuffered model
N traffic sources; Homogeneous, same activity factor 
Source rate = 1; Link capacity = C
TDM: N must be <= C Packet: N may be > C
Example: N=5; each having 20% activity
Average load = 5*0.2 = 1
But C=1 appears insufficient…

## Slide 23: Statistical mux analysis (ii) unbuffered model
Overflow probability
  Probability that, at a given instant of time (random), the link load is greater than the link capacity
  Implies packet loss if buffer=0
Example: N=5;
each having 20% activity;

## Slide 24
Statistical mux analysis (iii) unbuffered model
Packet loss probability
  Number of lost packets over number of offered packets
Offered packets
  N * average number of offered packets per source = N * 
Lost packets:
  If k <= C active sources, no packet loss
  If k > C, k-C lost packets
hence
Example: N=5; each having 20% activity;
N  = 1

## Slide 25
Loss vs overflow
Example: N=30;
each 20% activity;
N  = 6
for C>>N:
Overflow=good approx for loss.