## Slide 1
Random Access Performance the case of Aloha

## Slide 2: The question
Random Access Capacity
  Any terminal transmits randomly
    Transmission can be successful
    Or can be insuccessful because of collisions
Easier case: no carrier sense (ALOHA)
Intuition:
  If “little” traffic, limited collision but little throughput
  If “large” traffic, several transmissions, but a lot of collisions
  Is there some “maximum” performance case?

## Slide 3: Scenario
Packet size T
Station A
Packet size T
Station B
SUCCESS
Packet size T
Station A
Packet size T
Station B
COLLISION

## Slide 4: Modeling assumptions
Infinite stations
Frame arrival rate
  σ frames/second, Poisson
  S = σT frames/packet_time
Retransmission:
  A frame is retransmitted after collision, at random time, until it succeeds in being transmitted
  S = arrival rate = throughput!
Frame transmission rate
  Λ frames/second, Poisson
  G = Λ T frames/packet_time
  Includes “retransmission” load: G>S

## Slide 5: Probability of channel transmissions

## Slide 6: Vulnerability period: 2T
Packet size T
Station A
Station B
Station B
Station B
Station B
T
T
XXX
XXXXXXXXX
XXX
OK!

## Slide 7: Throughput
Offered traffic
  G frames/packtime
Successful transmission
  probability that, in one vulnerability period 2T, no frames are generated
Throughput = offered traffic x successful transmission probability
Chart: 
| 0 | 5.0000000000000017E-2 | 0.1 | 0.15000000000000008 | 0.2 | 0.25 | 0.3000000000000001 | 0.35000000000000009 | 0.40000000000000008 | 0.45000000000000007 | 0.5 | 0.54999999999999993 | 0.6000000000000002 | 0.65000000000000024 | 0.70000000000000029 | 0.75000000000000033 | 0.80000000000000038 | 0.85000000000000042 | 0.90000000000000024 | 0.95000000000000051 | 1.0000000000000002 | 1.0500000000000003 | 1.1000000000000003 | 1.1500000000000008 | 1.2000000000000004 | 1.2500000000000004 | 1.3000000000000005 | 1.3500000000000005 | 1.4000000000000006 | 1.4500000000000006 | 1.5000000000000007 | 1.5500000000000007 | 1.6000000000000012 | 1.6500000000000012 | 1.7000000000000013 | 1.7500000000000013 | 1.8000000000000009 | 1.8500000000000014 | 1.900000000000001 | 1.9500000000000011 | 2.0000000000000009
Valori Y | 0 | 0.045242 | 0.081873 | 0.11112 | 0.13406 | 0.15163 | 0.16464 | 0.1738 | 0.17973 | 0.18296 | 0.18394 | 0.18308 | 0.18072 | 0.17715 | 0.17262 | 0.16735 | 0.16152 | 0.15528 | 0.14877 | 0.14209 | 0.13534 | 0.12858 | 0.12188 | 0.1153 | 0.10886 | 0.10261 | 0.096556 | 0.090727 | 0.085134 | 0.079784 | 0.074681 | 0.069826 | 0.06522 | 0.060857 | 0.056735 | 0.052845 | 0.049183 | 0.045739 | 0.042504 | 0.039472 | 0.036631
Offered load G
Throughput S
S versus G curve – S(G)

## Slide 8: Maximum throughput

## Slide 9: Slotted Aloha
Packet size T
Station A
Station B
Station B
Station B
Time Slot T
Time Slot T
XXXXXXXXXXXXX
Vulnerability period = T

## Slide 10: Slotted Aloha improvements
Throughput doubled with respect to unslotted version.
Price to pay: SYSTEM complication (sync, etc)

## Slide 11: Random Access: instability!
Chart: 
| 0 | 5.0000000000000024E-2 | 0.1 | 0.15000000000000013 | 0.2 | 0.25 | 0.30000000000000021 | 0.3500000000000002 | 0.40000000000000008 | 0.45000000000000007 | 0.5 | 0.54999999999999993 | 0.60000000000000042 | 0.65000000000000058 | 0.70000000000000051 | 0.75000000000000056 | 0.8000000000000006 | 0.85000000000000064 | 0.90000000000000024 | 0.95000000000000062 | 1.0000000000000002 | 1.0500000000000003 | 1.1000000000000003 | 1.1500000000000012 | 1.2000000000000004 | 1.2500000000000004 | 1.3000000000000005 | 1.3500000000000005 | 1.4000000000000006 | 1.4500000000000006 | 1.5000000000000007 | 1.5500000000000007 | 1.6000000000000016 | 1.6500000000000017 | 1.7000000000000011 | 1.7500000000000011 | 1.8000000000000009 | 1.8500000000000019 | 1.9000000000000017 | 1.9500000000000017 | 2.0000000000000009
Valori Y | 0 | 0.045242 | 0.081873 | 0.11112 | 0.13406 | 0.15163 | 0.16464 | 0.1738 | 0.17973 | 0.18296 | 0.18394 | 0.18308 | 0.18072 | 0.17715 | 0.17262 | 0.16735 | 0.16152 | 0.15528 | 0.14877 | 0.14209 | 0.13534 | 0.12858 | 0.12188 | 0.1153 | 0.10886 | 0.10261 | 0.096556 | 0.090727 | 0.085134 | 0.079784 | 0.074681 | 0.069826 | 0.06522 | 0.060857 | 0.056735 | 0.052845 | 0.049183 | 0.045739 | 0.042504 | 0.039472 | 0.036631
Offered
load